## Clock configuration
### Double frequency blink when using DPLL0
Issue:

Loop: delay 1ms→ toggle LED
Running directly from XOSC1 (12MHz) is fine
Running XOSC1 through DPLL makes the CPU run twice the calculated speed

Solution: Use GCLK clock reference in DPLL settings.
### USB Clock sources
Clock requirements:
For low-speed communications: 1.5 Mbps +/- 1.5%.
For full-speed communications: 12 Mbps +/- 0.25%. (Datasheed 38.5.3 Page 1132)
Source: silabs.com
Issue:
DFLL48M is designed to be run off of the 32.768k External RTC.
32.768k Ultra Low Power Internal Oscillator works for USB Device (HOST not tested) Verify!
12M XTAL Oscillator divided (/) works for USB Device (HOST not tested) Verify!

Solution: Use GCLK clock reference in DPLL settings.

### How to verify clock setting when the MCU is running?
### Verified working USB clock setup