Grid4 Firmware Development Guide
Firmware development for ATSAMD51 Targets

# Target microcontroller: SAMD51
# Useful links:
# ATSAMD51N19A Product page
## Main features
Relevant features of the microcontroller that make it suitable for the Grid4 project.
### Operating conditions
The datasheet specifies 1.71V to 3.63V, -40°C to +105°C, DC to 120 MHz
### Power consumption
The datasheet specifies a nominal 65uA/MHz active power consumption.
Pcore = 0.065*120 = 7.8mA @120MHz
### Memories
ATSAMD51N19A has the most memory from the D51 family.
1 MB self programmable flash with ECC
256KB main memory (SRAM)
### High-Performance Peripherals
- 32-channel DMA
- QSPI up to 75MHz with execute-in-place support
- Full-Speed (12Mbps) USB2.0 (device and embedded host)
### System Peripherals
- 32-channel event system
- Up to 8 SERCOM interfaces (UART, I2C, SPI etc.)
- Dual 12-bit, 1 MSPS Analog-to-Digital Converter
- Dual 12-bit, 1 MSPS Digital-to-Analog Converter
# ATSAMD51 interfaces in the Grid4 design
The Grid uses most of the available peripheral interfaces of the SAMD51 platform.
## High-Performance Peripherals
### SERCOM
GRID Communication	GRID_X	4x SERCOM/UART
GRID Aux Communication	GRID_AUX	1x SERCOM/UART
Peripheral configuration	SYS_I2C	1x SERCOM/I2C
LED driver		1x SERCOM/UART/SPI ?
LCD driver (optional)		1x SERCOM/SPI

## System Peripherals
GRID Communication	GRID_X	4x SERCOM/UART
GRID Aux Communication	GRID_AUX	1x SERCOM/UART
Peripheral configuration	SYS_I2C	1x SERCOM/I2C
LED driver		1x SERCOM/UART/SPI ?
LCD driver (optional)		1x SERCOM/SPI

# Grid4 Firmware Overview
ADC → SRAM

ADC 16bit mode (x256 oversampling)	1MSPS/256 = 4KSPS
8 analog inputs per ADC channel	4KSPS/8 = 0.5KSPS effective

# ATSAMD51 SERCOM UART interface (K+F)
## TX Complete interrupt for packets
The following code shows that tx complete interrupt is only called after the whole packet is transferred.
static void tx_cb_GRID_AUX(const struct usart_async_descriptor *const io_descr)
{
struct io_descriptor *io;
static uint8_t example_GRID_AUX[2];
example_GRID_AUX[0] = 0x55;
example_GRID_AUX[1] = 0x11;
gpio_toggle_pin_level(LED0);
usart_async_get_io_descriptor(io_descr, &io);
io_write(io, example_GRID_AUX, 2);
}
# Clock Configuration
The target hardware has an 8 MHz ceramic resonator connected to XOSC1 on the microcontroller. All clock sources must be generated from the XOSC1 or the internal sources.
The SERCOM and ADC peripherals can run from a clock source of up to 100MHz.

# USART Configuration (GRID_X)
## Common settings
### Component settings
Driver	HAL:Driver:USART_Async
Mode	UART
Instance		As defined later!

### Clocks
Core	GCG 0 (120MHz)
Slow	GCG 3 (32.768kHz)

### Basic configuration
Receive buffer enable	True
Transmit buffer enable	True
Frame parity	False
Character size	8 bits
Stop bit	One stop bit
Baud rate	2000000	2000 for testing and debugging

### Advanced configuration
Default settings
### Component signals
Component name:	Instance:	Component Signal RX:	Component Signal TX:
GRID_AUX	SERCOM2	PB24	PB25
GRID_NORTH	SERCOM1	PA01	PA00
GRID_EAST	SERCOM0	PC16	PC17
GRID_SOUTH	SERCOM6	PC12	PC13
GRID_WEST	SERCOM4	PB09	PB08

# SPI Configuration (GRID_LED)
### Component settings
Driver	HAL:Driver:SPI_Master_Async
Instance	SERCOM7

### Clocks
Core	GCG 0 (120MHz)
Slow	GCG 3 (32.768kHz)

### Component signals
MISO	PB18	Not used
MOSI	PB21
SCK	PB20	Not used

### Basic configuration
Receive buffer enable	False
Character Size	8
Baud rate	4 000 000

### Advanced configuration
Default settings
# SYS_I2C Bus
SYS_I2C Bus is used to configure the USB interface chip and other miscellaneous peripheral controllers.
## Configuration
### Component settings
Driver	HAL:Driver:I2C_Master_Async
Mode	I2C Master Standard/Fast-mode
Instance	SERCOM5

### Clocks
Core	GCG 0 (120MHz)
Slow	GCG 3 (32.768kHz)

### Basic configuration
I2C Bus clock speed (Hz)	100000

### Advanced configuration
Default settings
### Component signals
SCL	PA22
SDA	PA23

# ADC_0 & ADC_1
ADC_0 and ADC_1 are used to read the analog user interface controls on the Grid4 modules.
On B16 and P16 modules two eight channel analog multiplexers are connected to the converters.
Address pins are MUX_A, MUX_B, MUX_C → PC19, PC20, PC21 respectively.
## Known issues
ADC fails to convert (result register is empty) if clock settings are incorrect
60MHz → ADCCLOCK does not work!
12MHz → ADCCLOCK works!
## To be confirmed
Averaging and oversampling with decimation to support up to 16-bit result.
Selectable sampling time
Loading factory calibration
## Understanding the ADC Clock and Sampling Rate
ADC runs off of Generic Clock Generator. ADC Prescaler divides the frequency (Div2, Div4… Div256)
Sampling takes one CLK_ADC cycle by default (can be set to more, may be useful!). After sampling the conversion takes another 12 cycles (for 12-bit result).
Example: “In order to obtain 1MSPS in 12-bit resolution with a sampling time length of four CLK_ADC cycles, fCLK_ADC must be 1MSPS * (4 + 12) = 16MHz. As the minimal division factor of the prescaler is 2, GCLK_ADC must be 32MHz.”
## Understanding Result Accumulation
The results of multiple, consecutive conversions can be accumulated.
## Understanding Oversampling and Decimation
To increase the resolution by n bits, 4n samples must be accumulated.
Result resolution	Number of samples to be averaged
13 bits	4 samples
14 bits	16 samples
15 bits	64 samples
16 bits	256 samples

## Understanding Offset and Gain Correction
The correction will introduce a latency of 13 CLK_ADC clock cycles. In free running mode this latency is introduced on the first conversion only, since its duration is always less than the propagation delay. In single conversion mode this latency is introduced for each conversion.
## Understanding Master-Slave operation
ADC1 will serve as a slave of ADC0 by writing a '1' to the Slave Enable bit in the Control A register of theADC1 instance (ADC1.CTRLA.SLAVEEN). When enabled, GCLK_ADC0 clock and ADC0 controls are internally routed to the ADC1 instance.
Is this syncronized dual channel sampling?
## Understanding Master-Slave operation
ADC1 will serve as a slave of ADC0 by writing a '1' to the Slave Enable bit in the Control A register of theADC1 instance (ADC1.CTRLA.SLAVEEN). When enabled, GCLK_ADC0 clock and ADC0 controls are internally routed to the ADC1 instance.

## ADC Configuration
### Component settings
Driver	HAL:Driver:ADC_Async
Instance	ADC0 & ADC1

### Clocks
ADC	GCG 0	Max 32MHz @1MSPS 12Bit

### Basic configuration
Conversion Result Resolution	12-bit	Check 16-bit (averaging)
Reference Selection
Prescaler configuration	Div2	Prescaled Clock =< 16MHz
Free Running Mode	False
Differential Mode	False
Positive Mux Input Selection	ADC AIN7 Pin	Instance: ADC_0
Negative Mux Input Selection	Internal ground

### Advanced configuration
Default settings
### Component signals
AIN/7	PA07	Instance: ADC_0
AIN/4	PC02	Instance: ADC_1